## Slide 1: Interconnect Parasitic Extraction
Speaker: Wenjian Yu
Tsinghua University, Beijing, China
Thanks to J. White, A. Nardi, W. Kao, L. T. Pileggi, Zhenhai Zhu

## Slide 2: Outline
Introduction to parasitic extraction
Resistance extraction
Capacitance extraction
Inductance and impedance (RLC) extraction

## Slide 3: Introduction to Parasitic Extraction

## Slide 4: Introduction
Interconnect: conductive path
Ideally: wire only connects functional elements (devices, gates, blocks, …) and does not affect design performance
This assumption was approximately true for “large” design, it is unacceptable for DSM designs
Slides courtesy A. Nardi, UC Berkeley

## Slide 5: Introduction
Real wire has:
  Resistance
  Capacitance
  Inductance
Therefore wiring forms a complex geometry that introduces capacitive, resistive and inductive parasitics. Effects:
  Impact on delay, energy consumption, power distribution
  Introduction of noise sources, which affects reliability
To evaluate the effect of interconnects on design
performance we have to model them
Slides courtesy A. Nardi, UC Berkeley

## Slide 6: Conventional Design Flow
Funct. Spec
Logic Synth.
Gate-level Net.
RTL
Layout
Floorplanning
Place & Route
Front-end
Back-end
Behav. Simul.
Gate-Lev. Sim.
Stat. Wire Model
Parasitic Extrac.
Slides courtesy A. Nardi, UC Berkeley

## Slide 7
From electro-magnetic analysis to circuit simulation
Parasitic extraction
/ Electromagnetic analysis
Thousands of R, L, C
Filament with uniform current
Panel with uniform charge
Model order
reduction
Reduced circuit

## Slide 8: Challenges for parasitic extraction
Parasitic Extraction
  As design get larger, and process geometries smaller than 0.35m, the impact of wire resistance, capacitance and inductance (aka parasitics) becomes significant
  Give rise to a whole set of signal integrity issues
Challenge
  Large run time involved (trade-off for different levels of accuracy)
  Fast computational methods with desirable accuracy

## Slide 9: Resistance Extraction

## Slide 10: Outline
Introduction to parasitic extraction
Resistance extraction
  Problem formulation
  Extraction techniques
  Numerical techniques
  Other issues
Capacitance extraction
Inductance and RLC extraction

## Slide 11: Resistance extraction
Problem formulation
  A simple structure
  Two-terminal structure
  Multi-terminal (port) structure
L
W
H
i
B
A
+
-
V
i
It’s a single R value
NxN R matrix

## Slide 12: Resistance extraction
Extraction techniques
  Square counting
  Analytical approximate formula
    For simple corner structure
  2-D or 3-D numerical methods
    For multi-terminal structure; current has irregular distribution
    Solve the steady current field for i under given bias voltages
    Set V1 = 1, others all zero,
flowing-out current
Repeating it with different settings

## Slide 13: Resistance extraction
Extraction techniques – numerical method
  How to calculate the flowing-out current ?
  Field equation and boundary conditions
Normal component is zero; current can not flow out
Laplace equation inside conductor:
E
divergence
Boundary conditions:
port surface : u is known
other surface:
The BVP of Laplace equation becomes solvable
Field solver

## Slide 14: Resistance extraction
Numerical methods for resistance extraction
  Methods for the BVP of elliptical PDE:
  Finite difference method
    Derivative -> finite difference:
    Generate sparse matrix; for ODE and PDE
  Finite element method
    Express solution with local-support basis functions
    construct equation system with Collocation or Galerkin method
    Widely used for BVP of ODE and PDE
  Boundary element method
    Only discretize the boundary, calculate boundary value
    Generate dense matrix with fewer unknowns
For elliptical PDE

## Slide 15: Resistance extraction
Where are expensive numerical methods needed ?
  Complex onchip interconnects:
    Wire resistivity is not constant
    Complex 3D geometry around vias
  Substrate coupling resistance in mixed-signal IC

## Slide 16: Resistance extraction
All these methods calculate DC resistance
  Suitable for local interconnects with small dimensions, or analysis under lower frequency
  R at high frequency: estimated with skin depth for simple geometry; extracted with complex methods along with L
Reference
  W. Kao, C-Y. Lo, M. Basel and R. Singh, “Parasitic extraction: Current state of the art and future trends,” Proceedings of IEEE, vol. 89, pp. 729-739, 2001.
  Xiren Wang, Deyan Liu, Wenjian Yu and Zeyi Wang, "Improved boundary element method for fast 3-D interconnect resistance extraction," IEICE Trans. on Electronics, Vol. E88-C, No.2, pp.232-240, Feb. 2005.

## Slide 17: Capacitance Extraction

## Slide 18: Outline
Introduction to parasitic extraction
Resistance extraction
Capacitance extraction
  Fundamentals and survey
  Volume discretization method
  Boundary element method
Inductance and RLC extraction

## Slide 19: Capacitance extraction
Problem formulation
  A parallel-plate capacitor
    Voltage:
    Q and –Q are induced on both plates; Q is proportional to V
    The ratio is defined as C: C=Q/V
    If the dimension of the plate is large compared with spacing d,
  Other familiar capacitors
coaxial capacitor
interdigital capacitor

## Slide 20: Capacitance extraction
Problem formulation
  Capacitance exists anywhere !
  Single conductor can have capacitance
    Conductor sphere
  N-conductor system, capacitance matrix is defined:
Coupling capacitance
Total capacitance
Electric potential

## Slide 21: Capacitance extraction
Interconnect capacitance extraction
  Only simple structure has analytical formula with good accuracy
  Different from resistance, capacitance is a function of not only wire’s own geometry, but its environments
  All methods have error except for considering the whole chip; But electrostatic has locality character
  Technique classification:
    analytical and 2-D methods
C /unit length
2-D method ignores 3-D effect, using numerical technique to solve cross section geometry
Shield; window
Stable model

## Slide 22: Capacitance extraction
Interconnect capacitance extraction
  analytical and 2-D methods
  2.5-D methods
  Commercial tools
    Task: full-chip, full-path extraction
    Goal: error 10%, runtime ~ overnight for given process
lateral
From “Digital Integrated Circuits”, 2nd Edition, Copyright 2002 J. Rabaey et al.
Error > 10%

## Slide 23: Capacitance extraction
Interconnect capacitance extraction
  Commercial tools(pattern-matching):
  Geometric parameter extraction
    According to given process, generate geometry patterns and their parameters
  Build the pattern library
    Field solver to calculate capacitances of pattern
    This procedure may cost one week for a given process
  Calculation of C for real case
    Chop the layout into pieces
    Pattern-matching
    Combine pattern capacitances
  Error: pattern mismatch, layout decomposition
Cadence - Fire & Ice
Synopsys - Star RCXT
Mentor - Calibre xRC

## Slide 24: Capacitance extraction
3-D numerical methods
  Model actual geometry accurately; highest precision
  Shortage: capacity, running time
  Current status: widely investigated as research topic; used as library-building tool in industry, or for some special structures deserving high accuracy
Motivation
  The only golden value
  Increasing important as technology becomes complicated
  Algorithms for C extraction can be directly applied to R extraction; even extended to handle L extraction

## Slide 25: Capacitance extraction
Technology complexity
  Dielectric configuration
    Conformal dielectric
    Air void
    Multi-plane dielectric
  Metal shape and type
    Bevel line
    Trapezoid cross-section
    Floating dummy-fill
They are the challenges, even for 3-D field solver

## Slide 26: Capacitance extraction
3-D numerical methods – general approach
  Set voltages on conductor; solve for Qi
  Global method to get the whole matrix
Classification
  Volume discretization: FDM, FEM
  Boundary integral (element) method
  Stochastic method
  Others – semi-analytical approaches
Raphael’s RC3 – Synopsys Q3D (SpiceLink) – Ansoft
FastCap, HiCap, QBEM
QuickCap - Magma
Solve the electrostatic field for u, then

## Slide 27
Slides courtesy J. White, MIT
Notes: I will give some technical details of the 3-D field solvers based on finite difference method, and two kinds of boundary element methods.

## Slide 28
Slides courtesy J. White, MIT
most

## Slide 29
Slides courtesy J. White, MIT

## Slide 30: Capacitance extraction
Volume methods
  What’s the size of simulation domain ?
  Two kinds of problem: finite domain and infinite domain
  Which one is correct ?
    3-D extraction is not performed directly on a “real” case
    In the chopping & combination procedure, both models used
    Because of attenuation of electric field, the results from two models can approach to each other
both in most time
Because of its nature, volume methods use finite-domain model

## Slide 31
Slides courtesy J. White, MIT
c
MoM (method of moment)
Method of virtual charge
Indirect boundary element method
inside alg. of FastCap

## Slide 32
Slides courtesy J. White, MIT
Panel charges contribute to the potential of center of panel d (a dielectric panel)

## Slide 33
Slides courtesy J. White, MIT

## Slide 34
Slides courtesy J. White, MIT

## Slide 35
Slides courtesy J. White, MIT

## Slide 36
Slides courtesy J. White, MIT
Multipole expansion with order l
l=0:

## Slide 37
Slides courtesy J. White, MIT
Sparse blocked matrix each block is dense

## Slide 38
Slides courtesy J. White, MIT
QuickCap FastCap HiCap QBEM Raphael

## Slide 39: Capacitance extraction
Reference
[1] W. Kao, C-Y. Lo, M. Basel and R. Singh, “Parasitic extraction: Current state of the art and future trends,” Proceedings of IEEE, vol. 89, pp. 729-739, 2001.
[2] Wenjian Yu and Zeyi Wang, “Capacitance extraction”, in Encyclopedia of RF and Microwave Engineering , K. Chang [Eds.], John Wiley & Sons Inc., 2005, pp. 565-576.
[3] K. Nabors and J. White, FastCap: A multipole accelerated 3-D capacitance extraction program, IEEE Trans. Computer-Aided Design, 10(11): 1447-1459, 1991.
[4] Y. L. Le Coz and R. B. Iverson, “A stochastic algorithm for high speed capacitance extraction in integrated circuits,” Solid State Electronics, 35(7): 1005-1012, 1992.
[5] J. R. Phillips and J. White, “A precorrected-FFT method for electrostatic analysis of complicated 3-D structures,” IEEE Trans. Computer-Aided Design, 16(10): 1059-1072, 1997
[6] W. Shi, J. Liu, N. Kakani and T. Yu, A fast hierarchical algorithm for three-dimensional capacitance extraction, IEEE Trans. Computer-Aided Design, 21(3): 330-336, 2002.
[7] W. Yu, Z. Wang and J. Gu, Fast capacitance extraction of actual 3-D VLSI interconnects using quasi-multiple medium accelerated BEM, IEEE Trans. Microwave Theory Tech., 51(1): 109-120, 2003.
[8] W. Shi and F. Yu, A divide-and-conquer algorithm for 3-D capacitance extraction, IEEE Trans. Computer-Aided Design, 23(8): 1157-1163, 2004.

## Slide 40: Inductance Extraction

## Slide 41: Outline
Basic
  Two laws about inductive interaction
  Loop inductance
Interconnect inductance extraction
  Partial inductance & PEEC model
  Frequency-dependent LR extraction - FastHenry

## Slide 42: Two inductive laws
Ampere’s Law
Magnetic field created by: currents in conductor loop, time-varying electric field
Curl operator
Integral form (derived via Stokes’ Law):
For 1D wire, field direction predicted with right-hand rule
Displacement current density
AC current flowing through capacitor
Notes: This is the differential expression of the Ampere’s law. B is magnetic induction intensity, j is current density, and E is electric field intensity.
This law reveals that magnetic field is created by current and time-varying electric fields

## Slide 43: Two inductive laws
Ampere’s Law (cont’d)
Ohmic current density
For integrated circuit, the second term is usually neglected
0.13m technology:
Transistor switching current: 0.3mA minimal spacing of conductor: 0.13 m maximal voltage difference: 2V minimal signal ramp time: 20ps
Displacement current density
0.130.26
Quasi-static assumption:
Decouples inductive and capacitive effects in circuit

## Slide 44: Two inductive laws
Faraday’s Law
Time-varying magnetic field creates induced electric field
Magnetic flux
This induced electric field exerts force on charges in b
Eind is a different field than the capacitive electric field Ecap, or electrostatic field:
Both electric fields have force on charge !

## Slide 45: Two inductive laws
Faraday’s Law (cont’d)
Induced voltage along the victim loop:
Orientation of the loop with respect to the Eind determines the amount of induced voltage.
Magnetic field effect on the orthogonal loop can be zero !
This is supposed to be the reason why the partial inductive coupling between orthogonal wires is zero

## Slide 46: Loop inductance
Three equations
Relationship between time-derivative of current and the induced voltage is linear as well:
All linear relationships
Mutual inductance; self inductance if a=b
There are inductors in IC as components of filter or oscillator circuits; There are also inductors not deliberately designed into IC, i.e. parasitic inductance

## Slide 47: Onchip interconnect inductance
Parasitic inductive effect
  An example
  Ringing behavior
  50% delay difference is 17%
Model magnetic interaction
  “chicken-and-egg” problem
Generate L coefficients for all loop pairs is impractical ! O(N4)
“Many of these loop couplings is negligible due to little current; but in general we need to solve for them to make an accurate determination”
Far end of active line
0.18 width, 1 length
# Possible current loop: O(N2)

## Slide 48: Onchip interconnect inductance
Partial inductance model
  Invented in 1908; introduced to IC modeling in 1972
  Definition: the relationship between the current of aggressor and the virtual loop which victim segment forms with infinity
  Loop L is sums of partial L’s of segments forming loop
Sij are -1 if exactly one of the currents in segments i and j is flowing opposite to the direction assumed when computing Lij, partial

## Slide 49: Onchip interconnect inductance
Partial inductance model
  Partial inductance is used to represent the loop interactions without prior knowledge of actual loops
  Contains all information about magnetic coupling
Partial element equivalent circuit (PEEC) model
  Include partial inductance, capacitance, resistance
  Model IC interconnect for circuit simulation
  Has sufficient accuracy up to now
A two-parallel-line example

## Slide 50: Onchip inductance extraction
To calculate partial inductance
  Formula for two straight segments:
  Analytical solution is quite involved even for simple geometry
  Numerical solution, such as Gaussian quadrature can be used, but may be time-consuming
  How about high-frequency effects ?
    Skin effect; proximity effect
    Path of least impedance -> least loop L
Assumptions: current is evenly distributed
Signal line & its return

## Slide 51: Inductance extraction
Related research directions
  Design solution to cope with inductive effects
    Limited current loop; inductive effect is reduced, or easy to be analyzed (calculating partial L is costly)
  Use partial inductance (PEEC model)
    Consider issues of circuit simulation
    Partial inductance brings dense matrix to circuit simulation; both extraction and simulation is computationally expensive
  Inductance extraction considering high-frequency
    Beyond the on-chip application
    MQS, EMQS, full-wave simulation
Has not good locality as C
Simplify the problem
Approaches of matrix sparsification
No L explicitly; just Z

## Slide 52: Frequency-dependent LR extraction
High frequency consideration
  nonuniform current distribution affects R
  Extract R and partial L together
  Capacitive effects analyzed separately (MQS)
  Due to the interaction of magnetic field, values of L and R both rely on environments, like capacitance
  Problem formulation:
Impedance extraction:
Mutual resistance becomes visible at ultra-high frequency
Terminal pairs:

## Slide 53: Frequency-dependent LR extraction
FastHenry of MIT
  Two assumptions: MQS; terminal pairs with known current direction
  Partitioned into filaments, current distributed evenly
If Vr is set,

## Slide 54: Frequency-dependent LR extraction
35 pins
FastHenry of MIT
  Solve equation system with multiple right-hand sides
  Multipole acceleration; preconditioned GMRES solver
  Application: package, wide onchip wires (global P/G, clock)
  Shortage: computational speed (#unknown); model inaccuracy; filament partition depends on frequency
30 pins

## Slide 55: Inductance extraction
Reference
[1] M. W. Beattie and L. T. Pileggi, “Inductance 101: modeling and extraction,” in Proc. Design Automation Conference, pp. 323-328, June 2001.
[2] M. Kamon, M. J. Tsuk, and J. K. White, “Fasthenry: a multipole-accelerated 3-D inductance extraction program,” IEEE Trans. Microwave Theory Tech., pp. 1750 - 1758, Sep 1994.
[3] Z. Zhu, B. Song, and J. White. Algorithms in Fastimp: a fast and wide-band impedance extraction program for complicated 3-D geometries. IEEE Trans. Computer-Aided Design, 24(7): 981-998, July 2005.
[4] W. Kao, C-Y. Lo, M. Basel and R. Singh, “Parasitic extraction: Current state of the art and future trends,” Proceedings of IEEE, vol. 89, pp. 729-739, 2001.
[5] http://www.rle.mit.edu/cpg/research_codes.htm (FastCap, FastHenry, FastImp)