## Slide 1: Digital Flow
Practice Verilog
Patrice Delpy 2017

## Slide 2: HDL Introduction
Hardware description language (HDL): allows designer to specify logic function .
Computer-aided design (CAD) tool produces or synthesizes the optimized gates.

## Slide 3: HDL to gates
Simulation
  Input values are applied to the circuit
  Outputs checked for correctness
  Millions of dollars saved by debugging in simulation instead of hardware
Synthesis
  Transforms HDL code into a netlist describing the hardware (a list of gates and the wires connecting them)
IMPORTANT:
When describing circuits using an HDL, it’s critical to think of the hardware the code should produce.

## Slide 4: Structural
Think like a circuit (hardware)
  Describe explicit connections between logic gates instantiated and connected to one others
  Similar to schematic
Changing a,b or e any time may immediately change c, d
Reversing statement order does nothing
Concurrent process
a
b
d
c
e

## Slide 5: Procedural
Describe circuit as algorithm, many possible circuit could have same behavior but different implementation
Think like C code
Describe how a function works but not how to build it (what the component does)
Order of statement is important
Let the syntheziser do the logic

## Slide 6
Designs that combine dataflow and algorithmic constructs are called RTL

## Slide 7: Blocking assignement
Procedural (blocking) assignments (=) are done sequentially in the order of the statements are written.
Evaluated and assigned in a single step
Execution flow within the procedure is blocked until the assignment is completed
A second assignment is not started until the preceding one is complete
x = a | b Evaluate a |b and assign result to x

## Slide 8: Non blocking assignment
Evaluted and assigned in two steps:
1 . The right hand side is evaluated immediately
2. The hand side is delayed until other evaluations in the current time step are completed
x <= a | b Evaluate a |b but defer assignment to x

## Slide 9: Non-blocking versus blocking
Non blocking Blocking
Value are assigned at the end of the block
All assignments are made in parallel, process flow is not blocked
Value is assigned immediately
Process waits until the first assignement is complete, it blocks progress

## Slide 10: Blocking (=) versus Non-blocking (<=)
Sequential
Parallel
Executed simultaneously
a = b and b = c (previous value)
D
Q
D
Q
c
b
a
CLK
CLK
shift register
D
Q
a
CLK
b
c
At each rising clock edge, b = a
After that c = b = a -> c = a
At each rising clock edge, b and c simultaneously
receive the old values of a, b and c

## Slide 11
Continous assignment: only drive wire
Procedural assignment: only drive reg , integer

## Slide 12
To ensure correct synthesis and simulation results:
use blocking (=) assignment for combinational logic
use non-blocking (<=) assignment for sequential logic
Do not mix both assignments in one procedure

## Slide 13: Blocking (=) versus Non-blocking (<=)
D
Q
D
Q
D
Q
D
Q
Q1
Q2
Q2
Q1
D
CLK
CLK
CLK
CLK
D
optional

## Slide 14
Combinational
Sequential
D
Q
sel
b
a
1
0
sel
1
0
clk
out
out
b
a

## Slide 16
http://www.syssec.ethz.ch/content/dam/ethz/special-interest/infk/inst-infsec/system-security-group-dam/education/Digitaltechnik_14/09_Verilog_Sequential.pdf
sequential code and combinational code in verilog

## Slide 17
Difference entre procedural et sequential
http://jatinganhotra.com/blog/2013/02/24/concurrent-and-sequential-statements-in-verilog/

## Slide 18: Concurrent Statements
Concurrent means that the operations described in each line take place in parallel. The commonly used concurrent constructs are gate instantiation and the continuous assignment statement.

## Slide 19: Sequential statements
Sequential statements are similar to statements in a normal programming language. A sequence of statements is regarded as describing operations that take place one after the other instead of at the same time.
All sequential Verilog statements must be inside a procedural block.
Sequential statements are placed inside a begin/end block and executed in sequential order within the block. However, the blocks themselves are executed concurrently.
Verilog statements outside any process block are interpreted as concurrent statements and different procedural blocks execute concurrently.

## Slide 20
Page vide

## Slide 21: HDL
What is the need for Hardware Description Language?
Modeling, Represent, And Simulate Digital Hardware
  Hardware Concurrency
  Parallel Activity Flow
  Semantics for Signal Value And Time
Special Constructs And Semantics
  Edge Transitions
  Propagation Delays
  Timing Checks

## Slide 22: Design block : basic unit
Verilog provides the concept of module
Describes the functionality of the design
Two types of modules:
  Behavioral: describe what a module does
  Structural: describe how a module is built from elementary gates
Design block
outputs
inputs

## Slide 23: Defining a module
A module is the main block in verilog
We first need to declare:
  name of the module
  types of its connections
  names of its connections
Verilog module
a
b
c
y

## Slide 24: Module example:

## Slide 25: Port declaration
Verilog keyword
  input, output,inout
We can also define busses :
  [range_start:range_end]
Size = 32 bits

## Slide 26: instance
There a two techniques:
Ordered port listing
Direct port instantiation

## Slide 27: Modeling approches

## Slide 28: Testbench
Module
Generating inputs
Generating inputs
Stimulus block
Testbench

## Slide 29: Register & Wire
Wire (net)
  Physical connection between components
  A wire does not store its value, it must be driven
  use “wire” in continuous assignment
  Default value is z
Register
  Register represent abstract storage elements
  Holds value until an new value is assigned to it (remain unchanged): event driven
  Used in procedural block
  Default value is x