## Slide 1
http://ic.sjtu.edu.cn/ic/dic/wp-content/uploads/sites/10/2013/04/CMOS-VLSI-design.pdf

## Slide 2: Introduction
Interconnect: conductive path
Ideally: wire only connects functional elements (devices, gates, blocks, …) and does not affect design performance
This assumption was approximately true for “large” design, it is unacceptable for sub- micrometer technology

## Slide 3
Interconnection => major role in the performance of systems
The wires are packed very closely together and thus a large fraction of their capacitance is to their neighbors.
A wire switches, it tends to affect its neighbor through capacitive coupling, this effect is called crosstalk.
  Signal integrity issues =>noise sources, delay, which affects reliability
Considering all of these factors, the Physical Design Layout is now as crucial task in the conception flow

## Slide 4: Interconnect modeling
A wire is a distributed circuit with a resistance and capacitance per unit length
Its behavior can be approximated with a number of lumped elements
To evaluate the effect of interconnects on design
performance we have to model them

## Slide 6: Outline
Introduction to parasitic extraction
Resistance extraction
Capacitance extraction

## Slide 7: Introduction

## Slide 8
Real wire has:
  Resistance
  Capacitance
  Inductance
Therefore wiring forms a complex geometry that introduces capacitive, resistive and inductive parasitics. Effects:
  Impact on delay, energy consumption, power distribution
  Introduction of noise sources, which affects reliability
To evaluate the effect of interconnects on design
performance we have to model them

## Slide 9: InterConnect modeling
A wire is a distributed circuit with a resistance and capacitance per unit length
Its behavior can be approximated with a number of lumped elements

## Slide 10
Parasitic Extraction
  As design get larger, and process geometries smaller than 0.35m, the impact of wire resistance, capacitance and inductance (parasitics) becomes significant
  Give rise to a whole set of signal integrity issues
Challenge
  Large run time involved (trade-off for different levels of accuracy)
  Fast computational methods with desirable accuracy

## Slide 11
Introduction to parasitic extraction
Resistance extraction
  Problem formulation
  Extraction techniques
  Numerical techniques
  Other issues
Capacitance extraction

## Slide 12
Problem formulation
    A simple structure
    Two-terminal structure
    Multi-terminal (port) structure
L
W
H
i
B
A
+
-
V
i
NxN R matrix

## Slide 13
Extraction techniques
  Square counting
  Analytical approximate formula
    For simple corner structure
  2-D or 3-D numerical methods
    For multi-terminal structure; current has irregular distribution
    Solve the steady current field for i under given bias voltages
    Set V1 = 1, others all zero,
flowing-out current
Repeating it with different settings

## Slide 14
Extraction techniques – numerical method
  Field Solver (Laplace equation – PDE – Boundary )

## Slide 15
Capacitance exists anywhere !
Single conductor can have capacitance
N – conductor system => capacitance matrix is defined

## Slide 16: Impact
Increase delay

## Slide 17: Impact
Crosstalk
http://www.eetimes.com/document.asp?doc_id=1275823
Cs
Cc

## Slide 18: Capacitance Extraction
  Different from resistance, capacitance is a function of not only wire’s own geometry, but its environments
m1
m3
m2
c23
c13
c12
For multiple conductors of any shapes and materials, and in any dielectric, there is a capacitance between any two conductors
Mutual cap between wires
Capacitance is often written as a symmetric matrix
C =
-c21
c22
-c23
-c31
-c32
c33
c11
-c12
-c13
Mutual capacitance between m1 and m2 is C12 = q1/v2

## Slide 19: Capacitance extraction
Geometric extraction – poor accuracy
3D numerical methods
FEM
Boundary element method
Stochastic method
Field Solver Q3D , Raphael, FastCap, Magma

## Slide 20
An interconnect is a thin-film wire that electrically connects 2 or more components in an integrated circuit.
Interconnects can introduce parasitic (unwanted) components of capacitance, resistance, and inductance. These “parasitics” detrimentally affect
  performance (e.g. propagation delay)
  power consumption
  reliability
As transistors are scaled down in size and the number of metal wiring layers increases, the impact of interconnect parasitics increases.
  Need to model interconnects, to evaluate their impact

## Slide 21: Effect of interconnect Scaling
Interconnect delay scales as square of L
  minimize interconnect length!
If W is large, then it does not appear in RwireCwire
  Capacitance due to fringing fields becomes more significant
  as W is reduced; Cwire doesn’t actually scale with W for small W
    Coupling capacitance (Cc) effects interwire spacing – loading, crosstalk

## Slide 22
B
Wire B has additional sidewall capacitance to neighboring wires
C
Wire C has additional capacitance to the wire above it
Wire A simply has capacitance (Cpp + Cfringe) to substrate
A
Si substrate
oxide

## Slide 23
Coupling capacitance virtually exists only between adjacent wires or crossing wires
Cx
Cx
Cx

## Slide 24
C : beetwen wire and substract
Cc: beetwen 2 wire
Post layout analysis : Parasitic extractor tool
Geometric extraction: poor accuracy
Field Solver :3D modeling – Physical approch
Good results
More precision => time processing increase
Use a compute farm
Methodology : Used in analog and Digital flow